## Slide 1: Bits, Bytes, and Integers 15-213: Introduction to Computer Systems 2nd and 3rd Lectures, Sep. 3 and Sep. 8, 2015
Instructors:
Randal E. Bryant and David R. O’Hallaron

## Slide 2: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 3: Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 4: For example, can count in binary
Base 2 Number Representation
  Represent 1521310 as 111011011011012
  Represent 1.2010 as 1.0011001100110011[0011]…2
  Represent 1.5213 X 104 as 1.11011011011012 X 213

## Slide 5: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 6: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8
Notes: 虚拟地址空间由机器字长决定

## Slide 7: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 8: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 9: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 10: Example: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j ∈ A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 11: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 ➙ 0xBE
    ~010000012 ➙ 101111102
  ~0x00 ➙ 0xFF
    ~000000002 ➙ 111111112
  0x69 & 0x55 ➙ 0x41
    011010012 & 010101012 ➙ 010000012
  0x69 | 0x55 ➙ 0x7D
    011010012 | 010101012 ➙ 011111012

## Slide 12: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p (avoids null pointer access)-防止空指针应用

## Slide 13: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p (avoids null pointer access)
Watch out for && vs. & (and || vs. |)…
one of the more common oopsies in
C programming

## Slide 14: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on left
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 15: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings
Summary

## Slide 16: Encoding Integers
short int x = 15213;
short int y = -15213;
C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Two’s Complement
Sign
Bit

## Slide 17: Two-complement Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 18: Numeric Ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 19: Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform specific

## Slide 20: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7

## Slide 21: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 22: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X
Mappings between unsigned and two’s complement numbers: Keep bit representations and reinterpret

## Slide 23: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
U2T
T2U

## Slide 24: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16

## Slide 25: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 26: Conversion Visualized
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Complement Range
Unsigned
Range
2’s Comp.  Unsigned
  Ordering Inversion
  Negative  Big Positive

## Slide 27: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;

## Slide 28: Casting Surprises
  0 0U == unsigned
  -1 0 < signed
  -1 0U > unsigned
  2147483647 -2147483648 > signed
  2147483647U -2147483648 < unsigned
  -1 -2 > signed
  (unsigned) -1 -2 > unsigned
  2147483647 2147483648U < unsigned
  2147483647 (int) 2147483648U > signed
Expression Evaluation
  If there is a mix of unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32: TMIN = -2,147,483,648 , TMAX = 2,147,483,647
Constant1 Constant2 Relation Evaluation
  0 0U
  -1 0
  -1 0U
  2147483647 -2147483647-1
  2147483647U -2147483647-1
  -1 -2
  (unsigned)-1 -2
  2147483647 2147483648U
  2147483647 (int) 2147483648U

## Slide 29: Summary Casting Signed ↔ Unsigned: Basic Rules
Bit pattern is maintained
But reinterpreted
Can have unexpected effects: adding or subtracting 2w
Expression containing signed and unsigned int
  int is cast to unsigned!!

## Slide 30: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 31: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 32: Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 33: Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small numbers yields expected behavior

## Slide 34: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Representations in memory, pointers, strings
Summary

## Slide 35: Unsigned Addition
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)

## Slide 36: Visualizing (Mathematical) Integer Addition
Integer Addition
  4-bit integers u, v
  Compute true sum Add4(u , v)
  Values increase linearly with u and v
  Forms planar surface
Add4(u , v)
u
v

## Slide 37: Visualizing Unsigned Addition
Wraps Around
  If true sum ≥ 2w
  At most once
0
2w
2w+1
UAdd4(u , v)
u
v
True Sum
Modular Sum
Overflow
Overflow

## Slide 38: Two’s Complement Addition
TAdd and UAdd have Identical Bit-Level Behavior
  Signed vs. unsigned addition in C:
  int s, t, u, v;
  s = (int) ((unsigned) u + (unsigned) v);
  t = u + v
  Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)

## Slide 39: TAdd Overflow
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
–2w –1
–2w
0
2w –1–1
2w–1
True Sum
TAdd Result
1 000…0
1 011…1
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
PosOver
NegOver

## Slide 40: Visualizing 2’s Complement Addition
Values
  4-bit two’s comp.
  Range from -8 to +7
Wraps Around
  If sum  2w–1
    Becomes negative
    At most once
  If sum < –2w–1
    Becomes positive
    At most once
TAdd4(u , v)
u
v
PosOver
NegOver

## Slide 41: Multiplication
Goal: Computing Product of w-bit numbers x, y
  Either signed or unsigned
But, exact results can be bigger than w bits
  Unsigned: up to 2w bits
    Result range: 0 ≤ x * y ≤ (2w – 1) 2 = 22w – 2w+1 + 1
  Two’s complement min (negative): Up to 2w-1 bits
    Result range: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
  Two’s complement max (positive): Up to 2w bits, but only for (TMinw)2
    Result range: x * y ≤ (–2w–1) 2 = 22w–2
So, maintaining exact results…
  would need to keep expanding word size with each product computed
  is done in software, if needed
    e.g., by “arbitrary precision” arithmetic packages

## Slide 42: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
Implements Modular Arithmetic
  UMultw(u , v) = u · v mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
UMultw(u , v)
• • •

## Slide 43: Signed Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
  Some of which are different for signed vs. unsigned multiplication
  Lower bits are the same
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
TMultw(u , v)
• • •

## Slide 44: Power-of-2 Multiply with Shift
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  (u << 5) – (u << 3) == u * 24
  Most machines shift and add faster than multiply
    Compiler generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
UMultw(u , 2k)
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 45: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k 
  Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
0
0
0
•••
0

## Slide 46: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 47: Arithmetic: Basic Rules
Addition:
  Unsigned/signed: Normal addition followed by truncate, same operation on bit level
  Unsigned: addition mod 2w
    Mathematical addition + possible subtraction of 2w
  Signed: modified addition mod 2w (result in proper range)
    Mathematical addition + possible addition or subtraction of 2w
Multiplication:
  Unsigned/signed: Normal multiplication followed by truncate, same operation on bit level
  Unsigned: multiplication mod 2w
  Signed: modified multiplication mod 2w (result in proper range)

## Slide 48: Why Should I Use Unsigned?
Don’t use without understanding implications
  Easy to make mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
  Can be very subtle
    #define DELTA sizeof(int)
    int i;
    for (i = CNT; i-DELTA >= 0; i-= DELTA)
    . . .

## Slide 49: Counting Down with Unsigned
Proper way to use unsigned as loop index
    unsigned i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
See Robert Seacord, Secure Coding in C and C++
  C Standard guarantees that unsigned addition will behave like modular arithmetic
    0 – 1  UMax
Even better
    size_t i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
  Data type size_t defined as unsigned value with length = word size
  Code will work even if cnt = UMax
  What if cnt is signed and < 0?

## Slide 50: Why Should I Use Unsigned? (cont.)
Do Use When Performing Modular Arithmetic
  Multiprecision arithmetic
Do Use When Using Bits to Represent Sets
  Logical right shift, no sign extension

## Slide 51: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 52: Byte-Oriented Memory Organization
Programs refer to data by address
  Conceptually, envision it as a very large array of bytes
    In reality, it’s not, but can think of it that way
  An address is like an index into that array
    and, a pointer variable stores an address
Note: system provides private address spaces to each “process”
  Think of a process as a program being executed
  So, a program can clobber its own data, but not that of others
• • •
00•••0
FF•••F

## Slide 53: Machine Words
Any given computer has a “Word Size”
  Nominal size of integer-valued data
    and of addresses
  Until recently, most machines used 32 bits (4 bytes) as word size
    Limits addresses to 4GB (232 bytes)
  Increasingly, machines have 64-bit word size
    Potentially, could have 18 EB (exabytes) of addressable memory
    That’s 18.4 X 1018
  Machines still support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 54: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 55: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8

## Slide 56: Byte Ordering
So, how are the bytes within a multi-byte word ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, Internet
    Least significant byte has highest address
  Little Endian: x86, ARM processors running Android, iOS, and Windows
    Least significant byte has lowest address

## Slide 57: Byte Ordering Example
Example
  Variable x has 4-byte value of 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 58: Representing Integers
Decimal: 15213
Binary: 0011 1011 0110 1101
Hex: 3 B 6 D
6D
3B
00
00
IA32, x86-64
3B
6D
00
00
Sun
int A = 15213;
93
C4
FF
FF
IA32, x86-64
C4
93
FF
FF
Sun
Two’s complement representation
int B = -15213;
long int C = 15213;
00
00
00
00
6D
3B
00
00
x86-64
3B
6D
00
00
Sun
6D
3B
00
00
IA32

## Slide 59: Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * allows treatment as a byte array
Printf directives:
%p: Print pointer
%x: Print Hexadecimal
typedef unsigned char *pointer;
void show_bytes(pointer start, size_t len){
size_t i;
for (i = 0; i < len; i++)
printf(”%p\t0x%.2x\n",start+i, start[i]);
printf("\n");
}

## Slide 60: show_bytes Execution Example
int a = 15213;
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux x86-64):
int a = 15213;
0x7fffb7f71dbc 6d
0x7fffb7f71dbd 3b
0x7fffb7f71dbe 00
0x7fffb7f71dbf 00

## Slide 61: Representing Pointers
Different compilers & machines assign different locations to objects
Even get different results each time run program
int B = -15213;
int *P = &B;
x86-64
Sun
IA32
EF
FF
FB
2C
AC
28
F5
FF
3C
1B
FE
82
FD
7F
00
00

## Slide 62: Representing Strings
char S[6] = "18213";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
IA32
Sun
31
38
32
31
33
00
31
38
32
31
33
00

## Slide 63: Integer C Puzzles
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0
(x|-x)>>31 == -1
ux >> 3 == ux/8
x >> 3 == x/8
x & (x-1) != 0
int x = foo();
int y = bar();
unsigned ux = x;
unsigned uy = y;
Initialization

## Slide 64: Bonus extras

## Slide 65: Application of Boolean Algebra
Applied to Digital Systems by Claude Shannon
  1937 MIT Master’s Thesis
  Reason about networks of relay switches
    Encode closed switch as 1, open switch as 0
A
~A
~B
B
Connection when
A&~B | ~A&B
A&~B
~A&B
= A^B

## Slide 66: Binary Number Property
w = 0:
  1 = 20
Assume true for w-1:
  1 + 1 + 2 + 4 + 8 + … + 2w-1 + 2w = 2w + 2w = 2w+1
Claim
1 + 1 + 2 + 4 + 8 + … + 2w-1 = 2w
= 2w

## Slide 67: Code Security Example
Similar to code found in FreeBSD’s implementation of getpeername
There are legions of smart people trying to find vulnerabilities in programs
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}

## Slide 68: Typical Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, MSIZE);
printf(“%s\n”, mybuf);
}

## Slide 69: Malicious Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, -MSIZE);
. . .
}
/* Declaration of library function memcpy */
void *memcpy(void *dest, void *src, size_t n);

## Slide 70: Mathematical Properties
Modular Addition Forms an Abelian Group
  Closed under addition
    0  UAddw(u , v)  2w –1
  Commutative
    UAddw(u , v) = UAddw(v , u)
  Associative
    UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  0 is additive identity
    UAddw(u , 0) = u
  Every element has additive inverse
    Let UCompw (u ) = 2w – u UAddw(u , UCompw (u )) = 0

## Slide 71: Mathematical Properties of TAdd
Isomorphic Group to unsigneds with UAdd
  TAddw(u , v) = U2T(UAddw(T2U(u ), T2U(v)))
    Since both have identical bit patterns
Two’s Complement Under TAdd Forms a Group
  Closed, Commutative, Associative, 0 is additive identity
  Every element has additive inverse

## Slide 72: Characterizing TAdd
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
(NegOver)
(PosOver)
u
v
< 0
> 0
< 0
> 0
Negative Overflow
Positive Overflow
TAdd(u , v)
2w
2w

## Slide 73: Negation: Complement & Increment
Claim: Following Holds for 2’s Complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…111 == -1
Complete Proof?
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1

## Slide 74: Complement & Increment Examples
x = 15213
x = 0

## Slide 75: Code Security Example #2
SUN XDR library
  Widely used library for transferring data between machines
void* copy_elements(void *ele_src[], int ele_cnt, size_t ele_size);
ele_src
malloc(ele_cnt * ele_size)

## Slide 76: XDR Code
void* copy_elements(void *ele_src[], int ele_cnt, size_t ele_size) {
/*
* Allocate buffer for ele_cnt objects, each of ele_size bytes
* and copy from locations designated by ele_src
*/
void *result = malloc(ele_cnt * ele_size);
if (result == NULL)
/* malloc failed */
return NULL;
void *next = result;
int i;
for (i = 0; i < ele_cnt; i++) {
/* Copy object i to destination */
memcpy(next, ele_src[i], ele_size);
/* Move pointer to next memory region */
next += ele_size;
}
return result;
}

## Slide 77: XDR Vulnerability
What if:
  ele_cnt = 220 + 1
  ele_size = 4096 = 212
  Allocation = ??
How can I make this function secure?
malloc(ele_cnt * ele_size)

## Slide 78: Compiled Multiplication Code
leaq (%rax,%rax,2), %rax
salq $2, %rax
C compiler automatically generates shift/add code when multiplying by constant
long mul12(long x)
{
return x*12;
}
t <- x+x*2
return t << 2;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 79: Compiled Unsigned Division Code
shrq $3, %rax
Uses logical shift for unsigned
For Java Users
  Logical shift written as >>>
unsigned long udiv8
(unsigned long x)
{
return x/8;
}
# Logical shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 80: Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when u < 0
0
0
1
0
0
0
•••
x
2k
/
x / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
RoundDown(x / 2k)
•••
Result:
.
Binary Point
0
•••

## Slide 81: Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)
  Compute as  (x+2k-1)/ 2k 
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
u
2k
/
 u / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect

## Slide 82: Correct Power-of-2 Divide (Cont.)
Divisor:
Dividend:
Case 2: Rounding
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result
•••
Incremented by 1
Incremented by 1

## Slide 83: Compiled Signed Division Code
testq %rax, %rax
js L4
L3:
sarq $3, %rax
ret
L4:
addq $7, %rax
jmp L3
Uses arithmetic shift for int
For Java Users
  Arith. shift written as >>
long idiv8(long x)
{
return x/8;
}
if x < 0
x += 7;
# Arithmetic shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 84: Arithmetic: Basic Rules
Unsigned ints, 2’s complement ints are isomorphic rings: isomorphism = casting
Left shift
  Unsigned/signed: multiplication by 2k
  Always logical shift
Right shift
  Unsigned: logical shift, div (division + round to zero) by 2k
  Signed: arithmetic shift
    Positive numbers: div (division + round to zero) by 2k
    Negative numbers: div (division + round away from zero) by 2k Use biasing to fix

## Slide 85: Properties of Unsigned Arithmetic
Unsigned Multiplication with Addition Forms Commutative Ring
  Addition is commutative group
  Closed under multiplication
    0  UMultw(u , v)  2w –1
  Multiplication Commutative
    UMultw(u , v) = UMultw(v , u)
  Multiplication is Associative
    UMultw(t, UMultw(u , v)) = UMultw(UMultw(t, u ), v)
  1 is multiplicative identity
    UMultw(u , 1) = u
  Multiplication distributes over addtion
    UMultw(t, UAddw(u , v)) = UAddw(UMultw(t, u ), UMultw(t, v))

## Slide 86: Properties of Two’s Comp. Arithmetic
Isomorphic Algebras
  Unsigned multiplication and addition
    Truncating to w bits
  Two’s complement multiplication and addition
    Truncating to w bits
Both Form Rings
  Isomorphic to ring of integers mod 2w
Comparison to (Mathematical) Integer Arithmetic
  Both are rings
  Integers obey ordering properties, e.g.,
    u > 0  u + v > v
    u > 0, v > 0  u · v > 0
  These properties are not obeyed by two’s comp. arithmetic
    TMax + 1 == TMin
    15213 * 30426 == -10030 (16-bit words)

## Slide 87: Reading Byte-Reversed Listings
Address Instruction Code Assembly Rendition
8048365: 5b pop %ebx
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
804836c: 83 bb 28 00 00 00 00 cmpl $0x0,0x28(%ebx)
Disassembly
  Text representation of binary machine code
  Generated by program that reads the machine code
Example Fragment
Deciphering Numbers
  Value: 0x12ab
  Pad to 32 bits: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse: ab 12 00 00